Semiconductor Devices
 Lab Session Report:
 Metal Oxide Semiconductor Field Effect Transistor
By ISSA SIDIBE
31/12/2023
Introduction :
This lab session aims to demonstrate MOSFET properties through software, enhancing our understanding of semiconductor devices' efficiency and quality for improved interpretation.
I. Preparation

Figure 1: doping view of the transistor
Figure 2: doping concentratration under source

Figure 3: electron concentration for Vg=0V

1. For an N-Channel MOSFET
The gate doping is P-type (on the figure below we notice that the fermi level is close to the valence band
the drain and source doping is N-type

Figure 4: energy band diagram

2. For the Silicon
electron affinity is : 4.17eV
Work function of the polysilicon is : 6eV
3. The flatband voltage is
Vfb = electron affinity(Si) - Work function(SC)
Vfb= -173meV
The threshold voltage
Vth= 0.38V

II.Simulation
1.the curve bellow (figure 5) show a Vth of 0.5 V
V th theorically is 0.38

Figure 5: electrical characteristic
2.Plots (see figure 3 for electron ceoncentration at Vg=0V )
 Here at Vg =3V the electron concentration has been highly increased

Figure 6: electron concentration for Vg= 3V

Figure 7: hole concentration
the slope is due to the depletion region from 0.24 to 0.36

III.SIMULATION

Figure 8: electrical charateristic Id(Vd,Vg) for different Vg
1. Determination of the maximum current density

Figure 9: current density and transconductance determination

The max current density has been evaluated for 0.5 uA/um (see figure
2. The transconductance
g= { %DELTA Id } over {%DELTA Vgs} ={ 0.2 mA } over { 1.1 V }=0.181 mS

IV.Extraction of the subtreshold slope

Figure 10: subtreshold slope deduction

a. From the previous figure we deduced that the slope is 0.087 with the ruler
b. the Drain Induced Barrier Lowering (DIBL)

Figure 11: Drain Induced Barrier Lowering deduction
DIBL={0.5mA} over {1.01V}=50mA/V
Conclusion :
The lab session employing Silvaco software proved instrumental in comprehensively exploring MOSFET characteristics. Through analysis of polarization, current density, transconductance, subthreshold slope, and the Drain Induced Barrier Lowering (DIBL) , we gained valuable insights into the intricate behaviors and performance metrics of MOSFETs. This hands-on experience illuminated the critical factors influencing their operation, contributing significantly to our understanding of semiconductor device behavior and potential optimizations for future applications.